## Slide 1: Professor Dimitrios Melissourgos
Midterm 1 Answers
CIS 337 - NETWORK SYSTEMS MANAGEMENT

## Slide 2: 37 students in 2 sections 68 questions 52 minutes average submission time 46 seconds per question average 70% average score (812 out of 1160) 833 out of 1160 median score

## Slide 4: 60.41% Correct

## Slide 5: L4, L3, L2 Headers
Layer 4
Transport Layer
TCP
Port Numbers
Layer 3
Network Layer
IP
IP Addresses
Layer 2
Data Link Layer
Ethernet
MAC Addresses
Notes: Source: NetworkLessons.com

## Slide 6: Encapsulation and Headers
[HTTP [HTML [“Congratulations! You’ve…”]]]
L2 Frame – Gets converted to binary
L2 Frame’s Data Field – L3 Packet
L3 Packet’s Data Field – L4 Segment
L4 Segment’s Data Field – L5 Packet

## Slide 7: Transport Layer Protocols
Transmission Control Protocol (TCP)
  Most common transport layer protocol
  PDU called a segment
  Used for reliable transmission of data
  160 - 192 bits (20 -24 bytes) of overhead
    Options field is not required
Destination Port
(16 bits)
Unused
(6 bits)
Source Port
(16 bits)
Sequence Number
(32 bits)
ACK number
(32 bits)
Header Length
(4 bits)
Flags
(6 bits)
Flow Control
(16 bits)
CRC-16
(16 bits)
Urgent Pointer
(16 bits)
Options
(32 bits)
User Data
(varies)

## Slide 8: Transport Layer Protocols
User Datagram Protocol (UDP)
  Operates at the transport layer
  PDU called a datagram
  Used in time-sensitive situations, for control messages, or when reliability is handled by the application layer
  32-64 bits (4-8 bytes) of overhead
    Source port is optional in IPv4 and IPv6, Checksum is optional in IPv4
Destination Port
(16 bits)
Source Port
(16 bits)
Length
(16 bits)
Checksum
(16 bits)
User Data
(varies)

## Slide 10: 92.09% Correct

## Slide 11: L4, L3, L2 Headers
Layer 4
Transport Layer
TCP
Port Numbers
Layer 3
Network Layer
IP
IP Addresses
Layer 2
Data Link Layer
Ethernet
MAC Addresses
Notes: Source: NetworkLessons.com

## Slide 13
 | Sender | PDU | Receiver
Application |  | Packet | 
Transport |  | Segment | 
Network |  | Packet | 
Data Link |  | Frame | 
Physical |  |  | 
TCP
HTTP
Request
Ethernet
IP
TCP
HTTP
Request
HTTP
Request
IP
TCP
IP
TCP
HTTP
Request
Ethernet
Ethernet
IP
TCP
HTTP
Request
IP
TCP
HTTP
Request
TCP
HTTP
Request
HTTP
Request
HTTP
Request

## Slide 14: Network Layer Protocols
Internet Protocol (IP)
  IP version 4 (IPv4)
    Most common version of IP used
    32-bit addresses (232 or ~4.29 billion possible)
    Exhaustion of address space
  IP version 6 (IPv6)
    128-bit addresses (2128 or ~3.4 × 1038 possible)
    Slowly being adopted due to IPv4 exhaustion

## Slide 16: 87.74% Correct

## Slide 17: Business Data Communications & Networking
Chapter 2
Application Layer

## Slide 18: The Web
Hypertext Transfer Protocol (HTTP)
  Standard protocol for communication between a web browser and a web server
HTTP Request
Client computer with Web browser software
HTTP Response
Web Server

## Slide 20: 69.73% Correct

## Slide 22: 79.82% Correct

## Slide 23: L4, L3, L2 Headers
Layer 4
Transport Layer
TCP
Port Numbers
Layer 3
Network Layer
IP
IP Addresses
Layer 2
Data Link Layer
Ethernet
MAC Addresses
Notes: Source: NetworkLessons.com

## Slide 25
 | Sender | PDU | Receiver
Application |  | Packet | 
Transport |  | Segment | 
Network |  | Packet | 
Data Link |  | Frame | 
Physical |  |  | 
TCP
HTTP
Request
Ethernet
IP
TCP
HTTP
Request
HTTP
Request
IP
TCP
IP
TCP
HTTP
Request
Ethernet
Ethernet
IP
TCP
HTTP
Request
IP
TCP
HTTP
Request
TCP
HTTP
Request
HTTP
Request
HTTP
Request

## Slide 27: 85.57% Correct

## Slide 29: Transport Layer Protocols
User Datagram Protocol (UDP)
  Operates at the transport layer
  PDU called a datagram
  Used in time-sensitive situations, for control messages, or when reliability is handled by the application layer
  32-64 bits (4-8 bytes) of overhead
    Source port is optional in IPv4 and IPv6, Checksum is optional in IPv4
Destination Port
(16 bits)
Source Port
(16 bits)
Length
(16 bits)
Checksum
(16 bits)
User Data
(varies)

## Slide 30
  Labs 3 and 5

## Slide 31: 62.58% Correct

## Slide 32: Network Layer Functions
Addressing
  IPv4 addresses are 32 bits
  Most common way to write is using dot-decimal notation
    Easier for people to read and remember
    Breaks the address into four bytes and writes each byte in decimal notation instead of binary
    Example: 129.79.78.193
10000001
01001111
01001110
11000001

## Slide 33: IPv4 Exhaustion
The Internet Corporation for Assigned Names and Numbers (ICANN) is the entity that creates and distributes all IP addresses
232 = 4,294,967,296 unique IP addresses
We have more devices than that
Notes: Similar to ASCII with 8 bits and UTF16 with 16 bits
Apple owns almost 18 million IPv4 addresses
The US owns about 37% of all IPv4 addresses
We use NAT to map external addresses to private addresses
The number of IPv4 are still not enough

## Slide 34: Network Protocols
IPv4 Packet
  160-192 bits (20-24 bytes) of overhead
  Options field rarely used
Header length
(4 bits)
Packet Offset
(13 bits)
Version number
(4 bits)
Type of service
(8 bits)
Total length
(16 bits)
IDs
(16 bits)
Flags
(3 bits)
Time to Live /
Hop Limit
(8 bits)
CRC-16
(16 bits)
Protocol
(8 bits)
Options
(32 bits)
User Data
(varies)
Source Address
(32 bits)
Destination Address
(32 bits)

## Slide 35: 45.5% Correct

## Slide 36: Transport Layer Protocols
User Datagram Protocol (UDP)
  Operates at the transport layer
  PDU called a datagram
  Used in time-sensitive situations, for control messages, or when reliability is handled by the application layer
  32-64 bits (4-8 bytes) of overhead
    Source port is optional in IPv4 and IPv6, Checksum is optional in IPv4
Destination Port
(16 bits)
Source Port
(16 bits)
Length
(16 bits)
Checksum
(16 bits)
User Data
(varies)

## Slide 37
  Lab 5

## Slide 38: 83.55% Correct

## Slide 39: The solution: IPv6
Notes: Source: vasexperts.com

## Slide 40: IPv4 vs IPv6

## Slide 41: Network Protocols
IPv6 Packet
  Fixed Header
  320 bits (40 bytes) of overhead
Traffic Class / Priority
(8 bits)
Version number
(4 bits)
Flow Label
(20 bits)
Payload length
(16 bits)
Next Header
(8 bits)
Hop Limit
(8 bits)
User Data
(varies)
Source Address
(128 bits)
Destination Address
(128 bits)
Optional Headers
  Optional Headers
    Hop-by hop options
    Destination options (with routing options)
    Routing
    Fragment
    Authentication
    Encapsulation Security Payload
    Destination options
    Mobility

## Slide 42: 74.46% Correct

## Slide 44: 76.87% Correct

## Slide 46: Email
Mail User Agent (email client)
  Application Layer software package run by client computer
  e.g., Outlook, Apple Mail, Thunderbird
Simple Mail Transfer Protocol (SMTP)
  Email client formats user email message into this protocol packet
  Includes sender address and destination address
Mail Transfer Agent (mail server software)
  Application layer software package e.g., Microsoft Exchange
  No interaction with user, MTAs transfer to other MTAs until destination is reached
IMAP and POP
  Protocols used for communication between email client and mail server
  SMTP covers message transmission between email client and mail servers

## Slide 47: 59.63% Correct

## Slide 48: Five Types of Multiplexing
Frequency Division Multiplexing (FDM)
Time Division Multiplexing (TDM)
Statistical Time Division Multiplexing (STDM)
Wavelength Division Multiplexing (WDM)
Inverse Multiplexing (IMUX)

## Slide 49: Multiplexing
FDM
IMUX
Circuit is divided into a series of separate channels, each transmitting on a different frequency (which prevents interference)
TDM
Two or more computers take turns on the shared circuit (time)
Multiplexing uses 1 high-speed circuit to transmit a set of several low-speed circuits
IMUX does the opposite
Combines several low-speed circuits to make them appear as 1 high-speed circuit to the user

## Slide 50: Multiplexing
STDM
WDM
Statistical: assumes only 2 computers will transmit at any time
  e.g., users pause to read the screen
Selection of transmission speed for multiplexed circuit is based on statistical analysis of usage of circuits to be multiplexed
Version of FDM used in fiber optic cables
Light has different frequencies (colors)
Instead of using just one color, send multiple through same fiber cable
Increases the capacity of existing fiber optic cable

## Slide 51: 18.02% Correct

## Slide 52: Five Types of Multiplexing
Frequency Division Multiplexing (FDM)
Time Division Multiplexing (TDM)
Statistical Time Division Multiplexing (STDM)
Wavelength Division Multiplexing (WDM)
Inverse Multiplexing (IMUX)

## Slide 53: Multiplexing
FDM
IMUX
Circuit is divided into a series of separate channels, each transmitting on a different frequency (which prevents interference)
TDM
Two or more computers take turns on the shared circuit (time)
Multiplexing uses 1 high-speed circuit to transmit a set of several low-speed circuits
IMUX does the opposite
Combines several low-speed circuits to make them appear as 1 high-speed circuit to the user

## Slide 54: Multiplexing
STDM
WDM
Statistical: assumes only 2 computers will transmit at any time
  e.g., users pause to read the screen
Selection of transmission speed for multiplexed circuit is based on statistical analysis of usage of circuits to be multiplexed
Version of FDM used in fiber optic cables
Light has different frequencies (colors)
Instead of using just one color, send multiple through same fiber cable
Increases the capacity of existing fiber optic cable

## Slide 55: 58.39% Correct

## Slide 56: Guided Media
Twisted-pair (TP) cable
  Insulated pairs of wires bundled together
  Wires twisted to reduce electromagnetic interference
    Because they run perpendicular at points
  Sometimes use additional shielding
  Used for telephones, LANs
  Distance up to 100 meters
  Inexpensive
Notes: License: Public Domain
URL: http://commons.wikimedia.org/wiki/File:UTP_cable.jpg
Author: Baran Ivo

## Slide 57: Guided Media
Coaxial cable
  Has a single copper core, plus outer insulation, shielding, and inner insulation
  Less prone to interference
  Inexpensive but more than TP
  Distance up to 2 km (1.2 miles)
  Used for Cable TV / Internet

## Slide 58: Guided Media
Fiber optic cable
  Optical core made of glass or plastic
  Data transmitted using light from lasers or LEDs
  Resistant to interference and corrosion
  Extremely fast data rates
  Expensive
  Distance of 500m – 100km
  Used for Backbone, long distance circuits (e.g., undersea cables)
Notes: License: CC By
URL: http://commons.wikimedia.org/wiki/File:MultimodeFiber.JPG
Author: Hhedeshian

## Slide 59: Wireless Media
Radio Transmission
  Wireless transmission of electromagnetic waves through air
  Each device on network has a radio transceiver operating at a specific frequency range
  Enables mobile network communication
  Your laptop uses this for wireless connection
  Distance depends on frequency and power
Notes: What are some well-known frequencies?

## Slide 60: Wireless Media
Microwave
  High-frequency radio communication
  Line of sight which may require large antennas and towers
  Affected by weather
  Distance: ~60 km (due to curvature of the earth)
Satellite
  Special form of microwave communication involving satellites in space
  Long distance leads to propagation delays
Notes: What do we use for intercontinental communication, cable (wired) or satellite (wireless)?

## Slide 61: 81.22% Correct

## Slide 62: Digital Transmission of Digital Data
Sender and receiver must agree upon:
  Set of symbols
    How bits are encoded as voltages or light pulses
    How to distinguish between 0 and 1 bits
  Symbol rate
    How often symbols are sent

## Slide 63: 66.15% Correct

## Slide 64: L4, L3, L2 Headers
Layer 4
Transport Layer
TCP
Port Numbers
Layer 3
Network Layer
IP
IP Addresses
Layer 2
Data Link Layer
Ethernet
MAC Addresses
Notes: Source: NetworkLessons.com

## Slide 65: 94.54% Correct

## Slide 67: 61.31% Correct

## Slide 68: Digital Transmission of Analog Data
Pulse-Code Modulation (PCM) converts analog to digital by:
  Sampling the analog signal at regular intervals
  Measuring the amplitude of each sample
  Encoding (quantizing) the amplitude as binary data
Reducing quantizing error can be done by:
  Sampling more frequently
  Using more levels of amplitude in encoding

## Slide 69: 67.15% Correct

## Slide 70: Digital Transmission of Digital Data
Five types of signaling techniques
  Unipolar
    no current = 0
    +5 volts = 1

## Slide 71: Digital Transmission of Digital Data
Five types of signaling techniques
  Bipolar NRZ (no return to zero)
    voltage is positive or negative, but not zero
    +5V = 1
    -5V = 0

## Slide 72: Digital Transmission of Digital Data
Five types of signaling techniques
  Bipolar RZ (return to zero)
  always returns to 0 after each bit
  -5V = 0
  +5V = 1
  Fewer synchronization errors

## Slide 73: Digital Transmission of Digital Data
Five types of signaling techniques
  Bipolar AMI (alternate mark inversion)
    No volt = 0
    1 alternates between +5V and -5V
    Double current signaling

## Slide 74: Digital Transmission of Digital Data
Five types of signaling techniques
  Manchester
    Binary phase shift keying (BPSK)
    voltage is positive or negative
    bits are indicated by a mid-bit transition
Notes: Ethernet uses this encoding

## Slide 75: 86.96% Correct

## Slide 76: Client-Based Architecture
Client contains presentation, application, and data access logic
Most common in the 1980s
CLIENT
SERVER
Data Storage
Presentation Logic
Application Logic
Data Access Logic

## Slide 77: 56.84% Correct

## Slide 78: Client-Server Architecture
Advantages
  More efficient because of distributed processing
  Allows hardware/software from different vendors to be used together
  Less bandwidth required
Disadvantages
  May be challenges in configuring hardware/software from different vendors to work together
  In many cases, middleware is required

## Slide 79: Client-Server Architecture
Middleware is software that sits between the application software on the client and the application layer on the server
  Translates for software from different vendors, allowing communication
  Traffic cop: manages message transfers between clients and servers which reduces the amount of processing required for client and server

## Slide 80: 69.92% Correct

## Slide 81: Which Architecture Is It?
Youtube
ChatGPT
Visiting a news website
BitTorrent
Online multiplayer game
Single player game
Notes: Youtube – Client/Server, thin client
ChatGPT – Host based
Visiting a news website - Client/Server, thin client
BitTorrent – Peer to peer
Online multiplayer game - Client/Server, thick client
Single player game – Client based

## Slide 82: Peer-to-Peer Architecture
An older architecture that became popular again with Napster, BitTorrent, etc.
All devices can act as client and server
CLIENT/SERVER
Presentation Logic
Application Logic
Data Access Logic
Data Storage
CLIENT/SERVER
Presentation Logic
Application Logic
Data Access Logic
Data Storage

## Slide 83: 72.68% Correct

## Slide 84: Transport Layer Functions
Linking to the application layer
  TCP/UDP may serve multiple application layer protocols
  Ports used to identify application (2-byte numbers)
  Many source/destination ports follow standards
  Common port standards
    HTTP: TCP port 80
    HTTPS: TCP port 443
    FTP: TCP ports 20 and 21
    SMTP: TCP port 25
    IMAP: TCP port 143
    POP3: TCP port 110 or port 995 (secure version)
    DNS: TCP or UDP port 53 (most commonly UDP)

## Slide 86
  Lab 4 question 2

## Slide 87: 56.06% Correct

## Slide 88: Transport Layer Functions
Linking to the application layer
  TCP/UDP may serve multiple application layer protocols
  Ports used to identify application (2-byte numbers)
  Many source/destination ports follow standards
  Common port standards
    HTTP: TCP port 80
    HTTPS: TCP port 443
    FTP: TCP ports 20 and 21
    SMTP: TCP port 25
    IMAP: TCP port 143
    POP3: TCP port 110 or port 995 (secure version)
    DNS: TCP or UDP port 53 (most commonly UDP)

## Slide 90: 82.11% Correct

## Slide 91: Transport Layer Functions
Session management
  A session can be thought of as a conversation between two computers or creating a virtual circuit
  Using a session to send data is also called connection-oriented messaging (TCP)
  Sending messages without establishing a session is connectionless messaging (UDP)
  TCP connections are opened using a three-way handshake
    SYN
    SYN-ACK
    ACK
  Sessions provide reliable end-to-end connections

## Slide 92
  Lab 4

## Slide 93
  Lab 4 questions 3 and 4

## Slide 94: 64.76% Correct

## Slide 95: Transport Layer Protocols
Transmission Control Protocol (TCP)
  Most common transport layer protocol
  PDU called a segment
  Used for reliable transmission of data
  160 - 192 bits (20-24 bytes) of overhead
    Options field is not required
Destination Port
(16 bits)
Unused
(6 bits)
Source Port
(16 bits)
Sequence Number
(32 bits)
ACK number
(32 bits)
Header Length
(4 bits)
Flags
(6 bits)
Flow Control
(16 bits)
CRC-16
(16 bits)
Urgent Pointer
(16 bits)
Options
(32 bits)
User Data
(varies)

## Slide 96: Network Protocols
IPv4 Packet
  160-192 bits (20-24 bytes) of overhead
  Options field rarely used
Header length
(4 bits)
Packet Offset
(13 bits)
Version number
(4 bits)
Type of service
(8 bits)
Total length
(16 bits)
IDs
(16 bits)
Flags
(3 bits)
Time to Live /
Hop Limit
(8 bits)
CRC-16
(16 bits)
Protocol
(8 bits)
Options
(32 bits)
User Data
(varies)
Source Address
(32 bits)
Destination Address
(32 bits)

## Slide 97: Transport Layer Functions
Segmenting
  Breaking up large files into smaller segments (and putting them back together)
  Segments may be passed individually to application layer or after reassembly
  How large are the segments?
    Size depends on the network and data link layer protocols
    Maximum Segment Size (MSS) is negotiated during TCP handshake
    e.g., if the maximum size of the data in an Ethernet frame is 1,500 bytes and TCP and IP use 20 byte headers, the maximum segment size is 1460 bytes
TCP header
IPv4 header
Ethernet Frame Data Size
1500 – 20 – 20 = 1460 bytes

## Slide 98: 92.86% Correct

## Slide 99: Reserved IP Addresses
Certain IP addresses within each class are reserved for special purposes:
  Class A: 0.0.0.0 (default route) and 127.0.0.1 (loopback).
  Class B: 169.254.0.0 to 169.254.255.255 (APIPA).
  Class C: 192.168.0.0 to 192.168.255.255 (Private IP addresses).
A default route is the route that takes effect when no other route is available for an IP destination address.
Any traffic that a computer program sends on the loopback network is addressed to the same computer.
APIPA (Automatic Private IP Addressing) is a feature in operating systems like Windows that allows computers to automatically configure an IP address and subnet mask when their DHCP server is unavailable.
Private IP addresses are reserved for home use.

## Slide 100: 42.4% Correct

## Slide 101
  Lab 2 section 3

## Slide 102: 93.48% Correct

## Slide 103: Reserved IP Addresses
Certain IP addresses within each class are reserved for special purposes:
  Class A: 0.0.0.0 (default route) and 127.0.0.1 (loopback).
  Class B: 169.254.0.0 to 169.254.255.255 (APIPA).
  Class C: 192.168.0.0 to 192.168.255.255 (Private IP addresses).
A default route is the route that takes effect when no other route is available for an IP destination address.
Any traffic that a computer program sends on the loopback network is addressed to the same computer.
APIPA (Automatic Private IP Addressing) is a feature in operating systems like Windows that allows computers to automatically configure an IP address and subnet mask when their DHCP server is unavailable.
Private IP addresses are reserved for home use.

## Slide 104: 46.74% Correct

## Slide 105: Transport Layer Functions
Linking to the application layer
  TCP/UDP may serve multiple application layer protocols
  Ports used to identify application (2-byte numbers)
  Many source/destination ports follow standards
  Common port standards
    HTTP: TCP port 80
    HTTPS: TCP port 443
    FTP: TCP ports 20 and 21
    SMTP: TCP port 25
    IMAP: TCP port 143
    POP3: TCP port 110 or port 995 (secure version)
    DNS: TCP or UDP port 53 (most commonly UDP)

## Slide 106: 60.41% Correct

## Slide 107: Public IP and Private IP

## Slide 108: 95.66% Correct

## Slide 109
  Lab 4 questions 3 and 4

## Slide 110
  Lab 4

## Slide 111: 71.28% Correct

## Slide 112: Transport Layer Functions
Linking to the application layer
  TCP/UDP may serve multiple application layer protocols
  Ports used to identify application (2-byte numbers)
  Many source/destination ports follow standards
  Common port standards
    HTTP: TCP port 80
    HTTPS: TCP port 443
    FTP: TCP ports 20 and 21
    SMTP: TCP port 25
    IMAP: TCP port 143
    POP3: TCP port 110 or port 995 (secure version)
    DNS: TCP or UDP port 53 (most commonly UDP)

## Slide 114: 89.91% Correct

## Slide 115: L4, L3, L2 Headers
Layer 4
Transport Layer
TCP
Port Numbers
Layer 3
Network Layer
IP
IP Addresses
Layer 2
Data Link Layer
Ethernet
MAC Addresses
Notes: Source: NetworkLessons.com

## Slide 117: 63.98% Correct

## Slide 118: Encapsulation and Headers
[HTTP [HTML [“Congratulations! You’ve…”]]]
L2 Frame – Gets converted to binary
L2 Frame’s Data Field – L3 Packet
L3 Packet’s Data Field – L4 Segment
L4 Segment’s Data Field – L5 Packet

## Slide 119: 91.31% Correct

## Slide 120: Network Models
Advantages of Layers
  Networking functionality is modular and the software/hardware at any layer can be more easily substituted
    E.g., substitute wired for wireless at the physical layer
  Easier to troubleshoot or make changes to one layer at a time
  Application developers only need to worry about the application layer in their programs
Disadvantages of Layers
  Inefficient because the encapsulation/de-encapsulation at each layer requires processing
  Inefficient because encapsulation in a PDU increases overhead at each layer
Notes: Packets become larger

## Slide 121: 91.31% Correct

## Slide 122: Network Models
Advantages of Layers
  Networking functionality is modular and the software/hardware at any layer can be more easily substituted
    E.g., substitute wired for wireless at the physical layer
  Easier to troubleshoot or make changes to one layer at a time
  Application developers only need to worry about the application layer in their programs
Disadvantages of Layers
  Inefficient because the encapsulation/de-encapsulation at each layer requires processing
  Inefficient because encapsulation in a PDU increases overhead at each layer
Notes: Packets become larger

## Slide 123: 79.82% Correct

## Slide 124: Network Models
Advantages of Layers
  Networking functionality is modular and the software/hardware at any layer can be more easily substituted
    E.g., substitute wired for wireless at the physical layer
  Easier to troubleshoot or make changes to one layer at a time
  Application developers only need to worry about the application layer in their programs
Disadvantages of Layers
  Inefficient because the encapsulation/de-encapsulation at each layer requires processing
  Inefficient because encapsulation in a PDU increases overhead at each layer
Notes: Packets become larger

## Slide 125: 67.56% Correct

## Slide 126: Host-Based Architecture
Server contains all components (“server-based”)
Common in the 1960s with mainframes and terminals
CLIENT
SERVER
Presentation Logic
Application Logic
Data Access Logic
Data Storage

## Slide 127: 89.91% Correct

## Slide 128: Transport Layer Functions

## Slide 129: 94.26% Correct

## Slide 130: Digital vs. Analog Data
Digital transmission involves discrete binary values (i.e., 0 or 1)
Analog transmission involves continuous waves

## Slide 131: 73.69% Correct

## Slide 132
Destination Port
(16 bits)
Unused
(6 bits)
Source Port
(16 bits)
Sequence Number
(32 bits)
ACK number
(32 bits)
Header Length
(4 bits)
Flags
(6 bits)
Flow Control
(16 bits)
CRC-16
(16 bits)
Urgent Pointer
(16 bits)
Options
(32 bits)
User Data
(varies)

## Slide 133: 73.3% Correct

## Slide 134: Transport Layer Protocols
User Datagram Protocol (UDP)
  Operates at the transport layer
  PDU called a datagram
  Used in time-sensitive situations, for control messages, or when reliability is handled by the application layer
  32-64 bits (4-8 bytes) of overhead
    Source port is optional in IPv4 and IPv6, Checksum is optional in IPv4
Destination Port
(16 bits)
Source Port
(16 bits)
Length
(16 bits)
Checksum
(16 bits)
User Data
(varies)

## Slide 135: 94.26% Correct

## Slide 136: Network Layer Functions
Dynamic addressing
  Configuring each device manually is time consuming
  Assigning addresses permanently can be inefficient when devices are not connected to network
  A server can be designated to supply IP addresses automatically
  Dynamic Host Configuration Protocol (DHCP)
    Most common protocol for dynamic addressing
    Device (e.g., laptop) sends out broadcast message requesting an IP address
    DHCP server responds with assigned network layer address and its subnet mask
    Addresses are “leased” for a length of time from a list of authorized addresses

## Slide 137: MAC Address
MAC stands for Media Access Control
Also known as Physical Address
Unique 12-digit hexadecimal number that identifies a device on a network
Looks like this: 00-B0-D0-63-C2-26
Each device has a unique MAC address
Decided during manufacturing and hard-coded on the chip

## Slide 138: 15.15% Correct

## Slide 139
  Lab 3

## Slide 140: 100% Correct

## Slide 141: Types of Routing
Centralized Routing
  Routing decisions made by one computer
  All computers are connected to this one computer
Decentralized Routing
  Decisions made by each node independently of one another
  Information needs to be exchanged to prepare routing tables

## Slide 142: 61.81% Correct

## Slide 143: Decentralized Routing
Static
  All computers make their own routing decisions
  Routing table manually configured by network managers in MANs and WANs
  One individual or committee develops for LANs and Backbone networks
  Local adjustments when computers added or removed
Dynamic
  Routing decisions made by individual computers
  Routing tables updated periodically
  Routers exchange information using protocols to update tables
  Used when there are multiple routes through a network

## Slide 144: 93.87% Correct

## Slide 146: 79.82% Correct

## Slide 147: Routing
Dynamic routing algorithms
  Distance vector: routers count the number of “hops” along a route
    Computers periodically exchange information about hop count, speed of the circuits in the route, and how busy they are
  Link state: computers or routers track the number of hops, circuit speed, and traffic congestion
    Opposed to just knowing the distance, determines how fast each possible route is
    Provides more reliable, up to date paths to destinations

## Slide 148: 27.14% Correct

## Slide 149: Routing Protocols
Routing Information Protocol (RIP)
  Dynamic distance vector protocol used in smaller networks
  Operation
    Network manager builds the routing table
    Routing tables broadcast periodically
    When new computers are added, router counts “hops” and selects the shortest route

## Slide 150: Routing Protocols
Open Shortest Path First (OSPF)
  Dynamic hybrid interior routing protocol
  Commonly used on the internet and large enterprise networks
  More reliable paths less burdensome to the network because only updates sent
  Uses the number of computers on the route, network traffic, and error rates to select the best route

## Slide 151: Routing Protocols
Enhanced Interior Gateway Routing Protocol (EIGRP)
  A dynamic hybrid interior routing protocol (developed by Cisco)
    Hybrid because some features act like distance vector and others like link-state protocols
  Commonly used inside organizations
  Records transmission capacity, delay time, reliability and load for all paths
  Keeps the routing tables for its neighbors and uses this information in its routing decisions as well

## Slide 152: Routing Protocols
If each network uses a different protocol internally, how are they able to communicate?
Border Gateway Protocol (BGP)
  Dynamic distance vector protocol used for exterior routing
  Far more complex than interior routing protocols so rarely used inside companies; hard to administer
  Provide routing info only on selected routes (e.g., preferred or best route)
  Used on the internet to exchange routing information between large sections (autonomous systems) of the internet

## Slide 153: 94.99% Correct

## Slide 154: Multicasting (Communication)
Unicast - one computer to another computer
Broadcast - one computer to all computers in the network
Multicast - one computer to a group of computers (e.g., videoconference)
  Same data needs to reach multiple receivers and avoid transmitting it once for each receiver
    In IP multicast, hosts dynamically join and leave multicast groups using Internet Group Management Protocol (IGMP)
    The multicast group is assigned a special IP address
      All messages with this IP address routed to onto the subnet that contains requesting computer
    If I decide to leave the videoconference, my computer sends an IGMP message to the computer performing routing to remove me from the multicast group.

## Slide 155: 66.93% Correct

## Slide 156: TCP/IP Example
When my computer dials into a TCP/IP network it must be given 4 pieces of info to operate, provided by DHCP server or config file
  Device’s own IP address
  Subnet mask
  IP address of default gateway (most commonly the router)
  IP address of at least one DNS server

## Slide 157: 66.8% Correct

## Slide 158: IPv4 Exhaustion
The Internet Corporation for Assigned Names and Numbers (ICANN) is the entity that creates and distributes all IP addresses
232 = 4,294,967,296 unique IP addresses
We have more devices than that
Notes: Similar to ASCII with 8 bits and UTF16 with 16 bits
Apple owns almost 18 million IPv4 addresses
The US owns about 37% of all IPv4 addresses
We use NAT to map external addresses to private addresses
The number of IPv4 are still not enough

## Slide 159: 62.58% Correct

## Slide 160: Transport Layer Protocols
User Datagram Protocol (UDP)
  Operates at the transport layer
  PDU called a datagram
  Used in time-sensitive situations, for control messages, or when reliability is handled by the application layer
  32-64 bits (4-8 bytes) of overhead
    Source port is optional in IPv4 and IPv6, Checksum is optional in IPv4
Destination Port
(16 bits)
Source Port
(16 bits)
Length
(16 bits)
Checksum
(16 bits)
User Data
(varies)

## Slide 161: 88.44% Correct

## Slide 162
  Lab 4

## Slide 163: 23.76% Correct

## Slide 164: Network Layer Functions
Dynamic addressing
  Configuring each device manually is time consuming
  Assigning addresses permanently can be inefficient when devices are not connected to network
  A server can be designated to supply IP addresses automatically
  Dynamic Host Configuration Protocol (DHCP)
    Most common protocol for dynamic addressing
    Device (e.g., laptop) sends out broadcast message requesting an IP address
    DHCP server responds with assigned network layer address and its subnet mask
    Addresses are “leased” for a length of time from a list of authorized addresses

## Slide 165: Multicasting (Communication)
Unicast - one computer to another computer
Broadcast - one computer to all computers in the network
Multicast - one computer to a group of computers (e.g., videoconference)
  Same data needs to reach multiple receivers and avoid transmitting it once for each receiver
    In IP multicast, hosts dynamically join and leave multicast groups using Internet Group Management Protocol (IGMP)
    The multicast group is assigned a special IP address
      All messages with this IP address routed to onto the subnet that contains requesting computer
    If I decide to leave the videoconference, my computer sends an IGMP message to the computer performing routing to remove me from the multicast group.

## Slide 166: 68.83% Correct

## Slide 167: Transport Layer Functions
Session management
  A session can be thought of as a conversation between two computers or creating a virtual circuit
  Using a session to send data is also called connection-oriented messaging (TCP)
  Sending messages without establishing a session is connectionless messaging (UDP)
  TCP connections are opened using a three-way handshake
    SYN
    SYN-ACK
    ACK
  Sessions provide reliable end-to-end connections

## Slide 168: 30.91% Correct

## Slide 169
  Lab 3

## Slide 170: 85.57% Correct

## Slide 171
Example app: UDP client
from socket import *
serverName = ‘hostname’
serverPort = 12000
clientSocket = socket(socket.AF_INET,
socket.SOCK_DGRAM)
message = raw_input(’Input lowercase sentence:’)
clientSocket.sendto(message,(serverName, serverPort))
modifiedMessage, serverAddress =
clientSocket.recvfrom(2048)
print modifiedMessage
clientSocket.close()
Python UDPClient
include Python’s socket
library
create UDP socket for server
get user keyboard
input
Attach server name, port to message; send into socket
print out received string and close socket
read reply characters from
socket into string

## Slide 172
Example app: TCP client
from socket import *
serverName = ’servername’
serverPort = 12000
clientSocket = socket(AF_INET, SOCK_STREAM)
clientSocket.connect((serverName,serverPort))
sentence = raw_input(‘Input lowercase sentence:’)
clientSocket.send(sentence)
modifiedSentence = clientSocket.recv(1024)
print ‘From Server:’, modifiedSentence
clientSocket.close()
Python TCPClient
create TCP socket for server, remote port 12000
No need to attach server name, port

## Slide 173: 86.96% Correct

## Slide 174: Socket programming with UDP
UDP: no “connection” between client & server
no handshaking before sending data
sender explicitly attaches IP destination address and port # to each packet
rcvr extracts sender IP address and port# from received packet
UDP: transmitted data may be lost or received out-of-order
Application viewpoint:
UDP provides unreliable transfer of groups of bytes (“datagrams”) between client and server

## Slide 175: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
reliable transfer over UDP:
  add reliability at application layer
  application-specific error recovery!

## Slide 176: TCP: Overview RFCs: 793,1122,1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) inits sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size

## Slide 177: 68.33% Correct

## Slide 178: Data Link Protocols
Ethernet
  Developed into a formal standard, IEEE 802.3ac
  Several versions in use today
  Uses contention media access control (handles when two computers try to transmit at the same time)
  Ethernet II Frame
Destination Address
(6 bytes)
CRC
(4 bytes)
Preamble & Delimiter
(8 bytes)
Source Address
(6 bytes)
Type
(2 bytes)
Data
(46-1500 bytes)
Interframe Gap
(12 bytes)

## Slide 179: 68.33% Correct

## Slide 180: Additional Terminology
Each communication protocol has both:
  Information bits – those used to convey the user’s meaning
  Overhead bits – used for error checking; used to mark the start and end of characters and packets
Transmission efficiency – determined by dividing the total number of information bits by the total bits in the transmission
Throughput – the total number of information bits received per second after accounting for overhead bits and retransmissions

## Slide 181: 7.93% Correct

## Slide 182: Additional Terminology
Each communication protocol has both:
  Information bits – those used to convey the user’s meaning
  Overhead bits – used for error checking; used to mark the start and end of characters and packets
Transmission efficiency – determined by dividing the total number of information bits by the total bits in the transmission
Throughput – the total number of information bits received per second after accounting for overhead bits and retransmissions

## Slide 183: 54.67% Correct

## Slide 184: Data Link Protocols
Ethernet
  Developed into a formal standard, IEEE 802.3ac
  Several versions in use today
  Uses contention media access control (handles when two computers try to transmit at the same time)
  Ethernet II Frame
Destination Address
(6 bytes)
CRC
(4 bytes)
Preamble & Delimiter
(8 bytes)
Source Address
(6 bytes)
Type
(2 bytes)
Data
(46-1500 bytes)
Interframe Gap
(12 bytes)

## Slide 185: 69.73% Correct

## Slide 186: Network Protocols
IPv4 Packet
  160-192 bits (20-24 bytes) of overhead
  Options field rarely used
Header length
(4 bits)
Packet Offset
(13 bits)
Version number
(4 bits)
Type of service
(8 bits)
Total length
(16 bits)
IDs
(16 bits)
Flags
(3 bits)
Time to Live /
Hop Limit
(8 bits)
CRC-16
(16 bits)
Protocol
(8 bits)
Options
(32 bits)
User Data
(varies)
Source Address
(32 bits)
Destination Address
(32 bits)

## Slide 187: Network Layer Functions
Addressing
  IPv4 addresses are 32 bits
  Most common way to write is using dot-decimal notation
    Easier for people to read and remember
    Breaks the address into four bytes and writes each byte in decimal notation instead of binary
    Example: 129.79.78.193
10000001
01001111
01001110
11000001

## Slide 188: 78.43% Correct

## Slide 189: 83.93% Correct

## Slide 190: Media Access Control
Contention
  Transmit whenever circuit is available with no centralized control
  Common in Ethernet LANs
  When devices transmit at the same time, a collision occurs
  Devices must be “polite” and follow these steps:
    “Listen” for traffic
    If another device is transmitting, wait to transmit
    Otherwise, transmit (and keep listening)
    If another device begins to transmit, stop and wait

## Slide 191: Media Access Control
Controlled access
  Common in wireless LANs
    Controlled by wireless access point
  Access Request Technique
    Each device must get “permission” to transmit, similar to raising a hand
  Polling
    Roll-call polling
      Central device (controller) determines which devices can transmit
      Each client is checked periodically to see if it needs to transmit
    Hub Polling (token passing)
      One device begins the poll and then passes it to another device until it reaches them all

## Slide 192: 64.96% Correct

## Slide 193: Error Detection
Receivers need to know when the data transmitted is not correct
Add “check value” (error detection value) to message
Check value produced by mathematical formula
Three error detection methods:
  Parity checking
  Checksum
  Cyclic redundancy checking
Message
Check Value

## Slide 194: Error Detection
Parity check
  1-bit check value
  Based on the number of 1’s in the message
    Even parity: number of 1’s remains even
    Odd parity: number of 1’s remains odd
  Simple, but only detects 50% of errors
Example (Even Parity)
Character: ‘A’
Binary: 01000001
Parity Bit: 0
Character: ‘C’
Binary: 01000011
Parity Bit: 1

## Slide 195: Error Detection
Checksum
  1-byte (typically) check value
  Checksum algorithms vary in the creation of check values
  Detects 95% of errors

## Slide 196: Error Detection
Cyclic redundancy check (CRC)
  Treats message as a single binary number
  Divides by a preset number
  Uses remainder as the check value
Preset number is chosen so that remainder is the correct number of bits
Modes:
  CRC-16 (~99.998% error detection rate)
  CRC-32 (>99.99999% error detection rate)

## Slide 197: Conclusions
Time was not an issue
I might be helping too much with labs
You clearly have questions
  Come to office hours
  Ask them in class
  Email me
Start studying early
Pay attention in class
Highest score 1034 out of 1160
  I will be curving the grades by 126 points